An Introduction to:
The muDAQ System
Joseph Lewis-Merrill
KGB Lab @ UCLA

---
Road Map
- What is a DAQ?
- How Do DAQs Work?
- What is muDAQ?
- How Do I Use muDAQ?

---
What is a DAQ?

---
What is a DAQ?
- DAQ : [“dak”] (n.) Short for Data AcQusition. A system that collects “real-world” data from external inputs and processes it for storage and/or transmission.
- Most modern DAQs are electronic, but an observer with a notebook and pen would also be a DAQ.

---
What is a DAQ?
- There are two types of electronic signal:
  - Analog – takes any value in a continuous range, typically changes smoothly in time.
  - Ex: Radio waves, AC/Mains power, many sensors
  - Data encoded by the instantaneous value

---
What is a DAQ?
- There are two types of electronic signal:
  - Digital – Takes one of two values, denoted as ON - OFF, 1 - 0, True - False, etc.
  - Ex: All digital electronics, DC power (always ON), a handful of sensors
  - Data encoded in binary
    - (eg. 1101 = 8 + 4 + 0 +1 = 13)

---
How Do DAQs Work​?

---
How Do DAQs Work​?
- Modern computers are almost exclusively digital
- Electronic sensors are almost exclusively analog
- We need a translator!
- Enter: The ADC (Analog to Digital Converter)

---
How Do DAQs Work​?
- The ADC takes a voltage input within a range (e.g. 0-10V) and discretizes it into N segments or bins.
- Each bin is addressed by a binary number with b bits (i.e. b = len(1101) = 4)
- The output is the binary number D that corresponds to the bin into which the input voltage falls
V_i
V_r

---
How Do DAQs Work​?
- How do we calculate the voltage input given the digital (binary) output?
- The resolution δV is typically given by
V _ {i} = V_r {D} over {2^b} + V_{min}
δV = {V_r} over {2^b}

---
How Do DAQs Work​?
- The ADC is the “heart” of the DAQ. Every analog signal must pass through it.
- The primary “quality” of the ADC is its resolution in bits, b, with higher resolutions typically being more expensive.

---
What is muDAQ?

---
What is muDAQ?
- muDAQ is:
  - ModUlar
  - Multi-Unit
  - Multi-Use
  - μ-second scale
  - and more!

---
What is muDAQ?
- muDAQ is a DAQ system built around open-source software and hardware, to the extent that is possible.
- It is meant to be cheap to implement, easy to use, and easy to extend

---
What is muDAQ?
- The muDAQ system has two parts:
- The Arduino – Captures analog signals with onboard ADC and transmits data via serial over USB
- The Computer – Receives data via serial over USB and processes/stores it for analysis

---
What is muDAQ?
- For the Arduino, we typically use the Artemis ATP by SparkFun. It has a 14-bit ADC and 10 analog pins.
- We also have the Arduino UNO and its SparkFun equivalent, which have 10-bit ADCs and 6 analog pins
- External ADC expansion boards are available (See Jewel’s Work)

---
What is muDAQ?
- Any computer with a USB port capable of running Python 3 is compatible (Linux, Max, Windows, Raspberry Pi etc.)
- Uses a single .JSON file to program collection routine
- More features being added regularly

---
How Do I Use muDAQ?

---
How Do I Use muDAQ?
- Connecting the hardware:
  - Make sure the Arduino is disconnected
  - Plug in sensors to analog ports (i.e. “A11”)
  - Plug the Arduino cable into the computer
  - LED lights should turn on

---
How Do I Use muDAQ?
- The .JSON Control File (or JCF) contains all of the information the collection script needs in order to collect the data you want.
- There are three levels:
  - High/Overarching
  - Device
  - Channel

---
How Do I Use muDAQ?
- High Level Settings:
  - Affect output at every level/are very general
  - Ex: Program name – string – name of the collection program (e.g. “Two plume monitor”)
  - Ex: data_file_prefix – string – path to the location the data should be stored, including the file prefix (e.g. “<path/to/dir>/two_plume”)

---
How Do I Use muDAQ?
- Device Level Settings:
  - Contained as a list in High Level Settings
  - Settings unique to each board like:
    - Baudrate (bits/second)
    - Port (location of USB device)
    - Device Name

---
How Do I Use muDAQ?
- Channel Level Settings:
  - Settings unique to each data stream/channel
  - Ex: pin_id: The number or string ID of the analog pin on the Arduino board to be sampled
  - Different channels can sample the same pin, if desired

---
How Do I Use muDAQ?
- The muDAQ code is available in a public git repo
- To run muDAQ do the following:
  - Navigate to the repo directory
  - Navigate to “controller_code/”
  - Run “muDAQ_controller.py <path/to/json/file>”
  - Data is saved in .CSV format

---
How Do I Use muDAQ?
- muDAQ also has some analysis tools built in under the “analysis_code” directory
- “time_series_plotter.py” can take as an option the path to a muDAQ formatted csv data and does some rudimentary plotting of the data.

---
Final Thoughts
- Setting up a system is simple! The thermistors are inexpensive, and attaching longer leads only requires simple soldering
- I’m happy to help set folks up with a basic system, walk through its usage in more detail, etc
- The system is built on open-source software and hardware to the extent possible. Feel free to use/duplicated/modify/distribute as desired