An Introduction to:
The muDAQ System
Joseph Lewis-Merrill
KGB Lab @ UCLA

---
Road Map
- What is a DAQ?
- How do DAQs Work?
- What is muDAQ?
- How Do I Use muDAQ?

---
What is a DAQ?
- DAQ : [“dak”] (n.) Short for Data AcQusition. A system that collects “real-world” data from external inputs and processes it for storage and/or transmission.
- Most modern DAQs are electronic, but an observer with a notebook and pen would also be a DAQ.

---
What is a DAQ?
- There are two types of electronic signal:
  - Analog – takes any value in a continuous range, typically changes smoothly in time.
  - Ex: Radio waves, AC/Mains power, many sensors
  - Data encoded by the instantaneous value

---
What is a DAQ?
- There are two types of electronic signal:
  - Digital – Takes one of two values, denoted as ON - OFF, 1 - 0, True - False, etc.
  - Ex: All digital electronics, DC power (always ON), a handful of sensors
  - Data encoded in binary
    - (eg. 1101 = 8 + 4 + 0 +1 = 13)

---
How do DAQs Work​?
- Modern computers are almost exclusively digital
- Electronic sensors are almost exclusively analog
- We need a translator!
- Enter: The ADC (Analog to Digital Converter)

---
How do DAQs Work​?
- The ADC takes a voltage input within a range (e.g. 0-10V) and discretizes it into N segments or bins.
- Each bin is addressed by a binary number with b bits (i.e. b = len(1101) = 4)
- The output is the binary number D that corresponds to the bin into which the input voltage falls
V_i
V_r

---
How do DAQs Work​?
- How do we calculate the voltage input given the digital (binary) output?
- The resolution δV is typically given by
V _ {i} = V_r {D} over {2^b} + V_{min}
δV = {V_r} over {2^b}

---
How do DAQs Work​?
- The ADC is the “heart” of the DAQ. Every analog signal must pass through it.
- The primary “quality” of the ADC is its resolution in bits, b, with higher resolutions typically being more expensive.

---
What is muDAQ?
- muDAQ is:
  - ModUlar
  - Multi-Unit
  - Multi-Use
  - μ-second scale
  - and more!

---
What is muDAQ?
- The muDAQ system has two parts:
- The Arduino – Captures analog signals with onboard ADC and transmits data via serial over USB
- The Computer – Receives data via serial over USB and processes/stores it for analysis

---
What is muDAQ?
- For the Arduino, we typically use the Artemis ATP by SparkFun. It has a 14-bit ADC and 10 analog pins.
- We also have the Arduino UNO and its SparkFun equivalent, which have 10-bit ADCs and 6 analog pins
- External ADC boards are available (See Jewel Abbate’s Work)

---
What is muDAQ?
muDAQ Structure

---
How Do I Use muDAQ?
Plugging Things In

---
How Do I Use muDAQ?
The JSON Control File

---
How Do I Use muDAQ?
Example Collection

---
How Do I Use muDAQ?
Brief Analysis