## Slide 1: An Introduction to: The muDAQ System Joseph Lewis-Merrill KGB Lab @ UCLA

## Slide 2: Road Map
What is a DAQ?
How Do DAQs Work?
What is muDAQ?
How Do I Use muDAQ?

## Slide 3: What is a DAQ?

## Slide 4: What is a DAQ?
DAQ : [“dak”] (n.) Short for Data AcQusition. A system that collects “real-world” data from external inputs and processes it for storage and/or transmission.
Most modern DAQs are electronic, but an observer with a notebook and pen would also be a DAQ.

## Slide 5: What is a DAQ?
There are two types of electronic signal:
  Analog – takes any value in a continuous range, typically changes smoothly in time.
  Ex: Radio waves, AC/Mains power, many sensors
  Data encoded by the instantaneous value

## Slide 6: What is a DAQ?
There are two types of electronic signal:
  Digital – Takes one of two values, denoted as ON - OFF, 1 - 0, True - False, etc.
  Ex: All digital electronics, DC power (always ON), a handful of sensors
  Data encoded in binary
    (eg. 1101 = 8 + 4 + 0 +1 = 13)

## Slide 7: How Do DAQs Work​?

## Slide 8: How Do DAQs Work​?
Modern computers are almost exclusively digital
Electronic sensors are almost exclusively analog
We need a translator!
Enter: The ADC (Analog to Digital Converter)

## Slide 9: How Do DAQs Work​?
The ADC takes a voltage input within a range (e.g. 0-10V) and discretizes it into N segments or bins.
Each bin is addressed by a binary number with b bits (i.e. b = len(1101) = 4)
The output is the binary number D that corresponds to the bin into which the input voltage falls

## Slide 10: How Do DAQs Work​?
How do we calculate the voltage input given the digital (binary) output?
The resolution δV is typically given by

## Slide 11: How Do DAQs Work​?
The ADC is the “heart” of the DAQ. Every analog signal must pass through it.
The primary “quality” of the ADC is its resolution in bits, b, with higher resolutions typically being more expensive.

## Slide 12: What is muDAQ?

## Slide 13: What is muDAQ?
muDAQ is:
  ModUlar
  Multi-Unit
  Multi-Use
  μ-second scale
  and more!

## Slide 14: What is muDAQ?
muDAQ is a DAQ system built around open-source software and hardware, to the extent that is possible.
It is meant to be cheap to implement, easy to use, and easy to extend

## Slide 15: What is muDAQ?
The muDAQ system has two parts:
The Arduino – Captures analog signals with onboard ADC and transmits data via serial over USB
The Computer – Receives data via serial over USB and processes/stores it for analysis

## Slide 16: What is muDAQ?
For the Arduino, we typically use the Artemis ATP by SparkFun. It has a 14-bit ADC and 10 analog pins.
We also have the Arduino UNO and its SparkFun equivalent, which have 10-bit ADCs and 6 analog pins
External ADC expansion boards are available (See Jewel’s Work)

## Slide 17: What is muDAQ?
Any computer with a USB port capable of running Python 3 is compatible (Linux, Max, Windows, Raspberry Pi etc.)
Uses a single .JSON file to program collection routine
More features being added regularly

## Slide 18: How Do I Use muDAQ?

## Slide 19: How Do I Use muDAQ?
Connecting the hardware:
  Make sure the Arduino is disconnected
  Plug in sensors to analog ports (i.e. “A11”)
  Plug the Arduino cable into the computer
  LED lights should turn on

## Slide 20: How Do I Use muDAQ?
The .JSON Control File (or JCF) contains all of the information the collection script needs in order to collect the data you want.
There are three levels:
  High/Overarching
  Device
  Channel

## Slide 21: How Do I Use muDAQ?
High Level Settings:
  Affect output at every level/are very general
  Ex: Program name – string – name of the collection program (e.g. “Two plume monitor”)
  Ex: data_file_prefix – string – path to the location the data should be stored, including the file prefix (e.g. “<path/to/dir>/two_plume”)

## Slide 22: How Do I Use muDAQ?
Device Level Settings:
  Contained as a list in High Level Settings
  Settings unique to each board like:
    Baudrate (bits/second)
    Port (location of USB device)
    Device Name

## Slide 23: How Do I Use muDAQ?
Channel Level Settings:
  Settings unique to each data stream/channel
  Ex: pin_id: The number or string ID of the analog pin on the Arduino board to be sampled
  Different channels can sample the same pin, if desired

## Slide 24: How Do I Use muDAQ?
The muDAQ code is available in a public git repo
To run muDAQ do the following:
  Navigate to the repo directory
  Navigate to “controller_code/”
  Run “muDAQ_controller.py <path/to/json/file>”
  Data is saved in .CSV format

## Slide 25: How Do I Use muDAQ?
muDAQ also has some analysis tools built in under the “analysis_code” directory
“time_series_plotter.py” can take as an option the path to a muDAQ formatted csv data and does some rudimentary plotting of the data.

## Slide 26: Final Thoughts
Setting up a system is simple! The thermistors are inexpensive, and attaching longer leads only requires simple soldering
I’m happy to help set folks up with a basic system, walk through its usage in more detail, etc
The system is built on open-source software and hardware to the extent possible. Feel free to use/duplicated/modify/distribute as desired